## Slide 1: COMPUTER INSTRUCTIONS

## Slide 2: INSTRUCTION FORMAT
An instruction format or instruction code is a group of bits used to perform a particular operation on the data stored in computer.
Processor fetches an instruction from memory and decodes the bits to execute the instruction.
Different computers may have their own instruction set.

## Slide 3: INSTRUCTION FORMAT
Instruction code is divided into two parts namely operation code and address of data.
 Operation code consisting group of bits to define an operation such as add, subtract, multiply etc.

## Slide 4: INSTRUCTION FORMAT
In an instruction format:
First 12 bits (0-11) specify an address.
Next 3 bits specify operation code (opcode).
Left most bit specify the addressing mode I
I = 0 for direct address
I = 1 for indirect address

## Slide 5: TYPES OF INSTRUCTIONS
The basic computer has three 16-bit instruction code formats:
Memory Reference Instructions
Register Reference Instructions
Input/Output Instructions

## Slide 6: Memory Reference Instructions
In Memory reference instruction:
First 12 bits(0-11) specify an address.
Next 3 bits specify operation code (opcode).
Left most bit specify the addressing mode I I = 0 for direct address
I = 1 for indirect address
(Opcode = 000 through 111)

## Slide 7: Memory Reference Instructions
In Memory reference instruction:

first 12 bits (0-11) specify an address.
The address field is denoted by three x’s (in hexadecimal notation) and is equivalent to 12-bit address.
The last mode bit of the instruction represents by symbol I.
When I = 0, the last four bits of an instruction have a hexadecimal digit equivalent from 0 to 6 since the last bit is zero (0).

When I = 1 the last four bits of an instruction have a hexadecimal digit equivalent from 8 to E since the last bit is one (1).

## Slide 8: Memory Reference Instructions
Hexadecimal code |  |  |  |  |  |  | 
Symbol | I = 0 | I = 1 | Description |  |  |  | 
AND | 0xxx | 8xxx | AND memory word |  | to | AC | 
ADD | 1xxx | 9xxx | ADD memory word |  | to | AC | 
LDA | 2xxx | Axxx | LOAD Memory word to AC |  |  |  | 
STA | 3xxx | Bxxx | Store content memory | of | AC |  | in
BUN | 4xxx | Cxxx | Branch unconditionally |  |  |  | 
BSA | 5xxx | Dxxx | Branch and save return address |  |  |  | 
ISZ | 6xxx | Exxx | Increment and Skip if zero |  |  |  | 

## Slide 9: Register Reference Instructions
In Register Reference Instruction:

First 12 bits (0-11) specify the register operation.
The next three bits equals to 111 specify opcode.
The last mode bit of the instruction is 0.
Therefore, left most 4 bits are always 0111 which is equal to hexadecimal 7.

## Slide 10: Register Reference Instructions
10
Symbol | Hexadecimal code | Description
CLA | 7800 | Clear AC
CLE | 7400 | Clear E
CMA | 7200 | Complement AC
CME | 7100 | Complement E
CIR | 7080 | Circulate right AC and E
CIL | 7040 | Circulate left AC and E
INC | 7020 | Increment AC
SPA | 7010 | Skip next instruction if AC positive
SNA | 7008 | Skip next instruction is AC is negative
SZA | 7004 | Skip next instruction is AC is 0
SZE | 7002 | Skip next instruction is E is 0
HLT | 7001 | Halt computer

## Slide 11: I/O Reference Instructions
In I/O Reference Instruction:

First 12 bits (0-11) specify the I/O operation.
The next three bits equals to 111 specify opcode.
The last mode bit of the instruction is 1.
Therefore, left most 4 bits are always 1111 which is equal to hexadecimal F.
11

## Slide 12: I/O Reference Instructions
12
Symbol | Hexadecimal code | Description
INP | F800 | Input character to AC
OUT | F400 | Output character from AC
SKI | F200 | Skip on input flag
SKO | F100 | Skip on Output flag
ION | F080 | Interrupt on
IOF | F040 | Interrupt off