## Slide 1: 8086 microprocessor

## Slide 2: Features of 8086 microprocessor
It is 16-bit microprocessor
It has a 16-bit data bus
  So it can read/write data to memory
It has 20-bit address bus
  Can access up to 220 memory (1mb)
Support up to 64k I/O ports
Provides 14, 16-bit registers
It has multiplexed address and data bus
  AD0 – AD15 & A16 – A19
Its supports 2 modes of operations
  MIN MODES
  MAX MODES

## Slide 3: Architecture of 8086 microprocessor
Its divided into two independent functional units.
  BIU (Bus Interface Unit)
  EU (Execution Unit)
Dividing the work between these two units speed up processing.

## Slide 4: Execution Unit (EU)
8086 microprocessor architecture has 16bit.
4 general-purpose registers.
  AX, BX, CX, DX,
  and those can be a divide in to AH, AL, BH, BL, CH, CL, DH, DL.
A pipeline is a method that can fetch data from memory while executing an instruction. Without a pipeline, the system can do one thing at a time.
That means to fetch, decode, and execute then fetch the next instruction decode and execute.
The EU has a 16-bit arithmetic logic unit (ALU) which can add, subtract, AND, OR, XOR, increment, decrement, complement or shift binary numbers.
The main functions of EU are:
  Decoding
  Execution

## Slide 5: Execution Unit (EU)
The EU contains the following 16-bit registers:
  AX – Accumulator
  BX – Base Register
  CX – Count Register
  DX – Data Register
  SP – Stack Pointer
  BP – Base Pointer
  SI – Source Index Register
  DI – Destination Index Register
The AX, BX, CX and DX registers can be considered as two 8-bit registers.
  High byte
  Low byte
AX  AH, AL
BX  BH, BL
CX  CH, CL
DX  DH, DL

## Slide 6: Pointers and Index Registers
IP – Instruction pointer store memory location of next instruction to be executed (code segment)
BP – Base pointer (data segment)
SP – Stack pointer (stack segment)
SI – Source index (source data in data segment)
DI – Destination index (destination in data or extra segment)
  The index registers are particularly useful for string manipulation.

## Slide 7: Flags Registers

## Slide 8: Bus Interface Unit (BIU)
BIU calculates physical address by using segment address and offset address.
  [ Physical address = segment address * 10H + Offset address ]
BIU fetch data from memory when the pre-fetch queue has two-byte of space.
Then fetch data from memory and store at the pre-fetch queue.
The pre-fetch queue can hold six-byte data.
      Why six-bytes..?
  The reason is 8086 instruction’s maximum size is 6 byte then the queue can hold any instruction.

## Slide 9: Segment Registers
The 8086 architecture uses the concept of segmented memory.
  Memory capacity – 1mb
  Divided into 16 logical segments
  Each one Contains 64kb
There are 4 segment registers
  Code segment register(CS) –addressing memory location
  Data segment register(DS) –point to the data segment
  Extra segment register(ES)
  Stack segment register(SS)

## Slide 10: How instruction flow-through 8086 architecture

## Slide 11: 8086 - Pin Diagram

## Slide 12: 8086 - Pin Configuration
GND : Larger currents to the ground.
AD14-AD0, AD15 : These lines are called multiplexed lines.
NMI : its not user controlled, its reach processor when interrupts generates once.
INTR : its user controlled, we can enable / disable.
CLK : its signal used for synchronization between processor and all components

## Slide 13: 8086 - Pin Configuration
READY : active high pin(logic 1), used by the external peripherals.
  READY = 0 (ready for accept data)
  READY = 1 (not ready for accept data)
TEST : this pin is used along with wait instruction.
QS1&QS2 : it gives the status & instructions Queue
  Qs1 Qs0 Meaning
  0 0 No operation
  0 1 first byte of opcode from Queue
  1 0 Queue is cleared
  1 1 next byte of opcode from Queue

## Slide 14: 8086 - Pin Configuration
S0’, S1’, S2’ : This indicates the type of operations carried out by the processor.
  S0’ S1’ S2’ FUNCTION
  0 0 0 interrupts acknowledge
  0 0 1 I/O read
  0 1 0 I/O write
  0 1 1 Halt (not doing anything)
  1 0 0 opcode fetch
  1 0 1 memory read
  1 1 0 memory write
  1 1 1 passive (ideal state)

## Slide 15: 8086 - Pin Configuration
LOCK’ : its going for lock the system bus.
  LOCK = 0
  LOCK = 1
R1’/GT1’ /,R0’/GTO’ (request/grant) : In case of MAX mode if multiple processor are connect if the other processor wants to access the bus.
MN/MX’ : selecting min mode / max mode
  Pin connected to VCC /programmed to 1  MIN MODE
  Pin connected to GROUND  MAX MODE

## Slide 16: 8086 - Pin Configuration
BHE’/S7 : bus high enable
  Its representing what type of data processor accessing.
  BHE A0 INDICATION
  0 0 whole word (64k)
  0 1 upper data/ from odd bank
  1 0 lower data/ from even bank
  1 1 none
A19/S6 – A16/S3 : address/ status bus (multiplexed)
  S6 : always remains logic 0
  S5 : indicate condition of FLAG bits

## Slide 17: 8086 - Pin Configuration
S4, S3 : represent which segment is currently the processor accessing.
  S4 S3 Segment
  0 0 ES
  0 1 SS
  1 0 CS
  1 1 DS
RD’ : read signal is active low pin (logic =0)
VCC : MAX voltage we can give at here is +5.0 V

## Slide 18: Thank You!!