## Slide 1: Register Transfer Language and Micro operation

## Slide 2: Register Transfer and Micro operations
Register Transfer Language
Register Transfer
Arithmetic Micro-operations
Logic Micro-operations
Shift Micro-operations
Register Transfer
Bus and Memory Transfers

## Slide 3: Register transfer language
A specific notation used to specify the digital system is called register transfer language.
For any function of the computer, the register transfer language can be used to describe the (sequence of) micro-operations.
Register transfer language
  A symbolic language
  A convenient tool for describing the internal organization ofdigital computers
  Can also be used to facilitate the design process of digital systems

## Slide 4: Micro-operations
Simple digital systems are frequently characterized in terms of
  the registers they contain, and
  the operations that they perform.
The operations on the data in registers are called micro- operations.
The functions built into registers are examples of micro-
operations
  Shift
  Load
  Clear
  Increment ...etc.

## Slide 5: Micro-operations
Computer system micro-operations are of four types:
  Register transfer micro-operations
  Arithmetic micro-operations
  Logic micro-operations
  Shift micro-operations

## Slide 6: Register Transfer
Copying the contents of one register to another is a register transfer
A register transfer is indicated as R2  R1
  In this case the contents of register R1 are moved into register R2.
  A simultaneous transfer of all bits from the source R1 to the destination register R2, during one clock pulse.
  Note that this is a destructive; i.e. the contents of R1 are not altered by copying (loading) them to R2.

## Slide 7: Arithmetic Micro-operations
R3  R1 + R2 | Contents of R1 plus R2 transferred to R3
R3  R1 - R2 | Contents of R1 minus R2 transferred to R3
R2  R2’ | Complement the contents of R2
R2  R2’+ 1 R3  R1 + R2’+ 1 | 2's complement the contents of R2 (negate) subtraction
R1  R1 + 1 | Increment
R1  R1 - 1 | Decrement
The basic arithmetic micro-operations are
  Addition
  Subtraction
  Increment
  Decrement
The additional arithmetic micro-operations are
  Add with carry
  Subtract with borrow
  Transfer/Load
  etc. …
Summary of Typical Arithmetic Micro-Operations

## Slide 8: Arithmetic circuit
S1 | S0 | Cin | Y | Output | Microoperation
0 | 0 | 0 | B | D = A + B | Add
0 | 0 | 1 | B | D = A + B + 1 | Add with carry
0 | 1 | 0 | B’ | D = A + B’ | Subtract with borrow
0 | 1 | 1 | B’ | D = A + B’+ 1 | Subtract
1 | 0 | 0 | 0 | D = A | Transfer A
1 | 0 | 1 | 0 | D = A + 1 | Increment A
1 | 1 | 0 | 1 | D = A - 1 | Decrement A
1 | 1 | 1 | 1 | D = A | Transfer A

## Slide 9: Logical micro-operations
Specify binary operations on the strings of bits in registers.
– Logic micro-operations are bit-wise operations, i.e., they work on the individual bits of data.
There are, in principle, 16 different logic functions that can be defined over two binary input variables.
However, most systems only implement four of these
– AND (), OR (), XOR (), Complement/NOT
The others can be created from combination of these
A | B | F0 | F1 | F2 | … | F13 | F14 | F15
0 | 0 | 0 | 0 | 0 | … | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | … | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | … | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | … | 1 | 0 | 1

## Slide 10: Logical Micro-operations
x y | 0 0 1 1 0 1 0 1 | Boolean Function | Micro- Operations | Name
 | 0 0 0 0 0 0 0 1 0 0 1 0 0 0 1 1 0 1 0 0 0 1 0 1 0 1 1 0 0 1 1 1 1 0 0 0 1 0 0 1 1 0 1 0 1 0 1 1 1 1 0 0 1 1 0 1 1 1 1 0 1 1 1 1 | F0 = 0 F1 = xy F2 = xy' F3 = x F4 = x'y F5 = y F6 = x  y F7 = x + y F8 = (x + y)' F9 = (x  y)' F10 = y' F11 = x + y' F12 = x' F13 = x' + y F14 = (xy)' F15 = 1 | F  0 F  A  B F  A  B’ F  A F  A’ B F  B F  A  B F  A  B F  A  B)’ F  (A  B)’ F  B’ F  A  B F  A’ F  A’ B F  (A  B)’b F  all 1's | Clear AND Transfer A Transfer B Exclusive-OR OR NOR Exclusive-NOR Complement B Complement A NAND Set to all 1's
List of Logic Micro-operations
  16 different logic operations with 2 binary vars.
  n binary vars → 2 2 n functions
Truth tables for 16 functions of 2 variables and the corresponding 16 logic micro-operations

## Slide 11: Hardware implementation of logic Micro-operation
Function table
S 1
S 0
F i
Ai Bi
0
1
4 X 1 MUX
2
3 Select
S1 | S0 | Output | -operation
0 | 0 | F = A  B | AND OR XOR Complement
0 | 1 | F = A  B | 
1 | 0 | F = A  B | 
1 | 1 | F = A’ | 

## Slide 12: SHIFT MICRO OPERATIONS
There are three types of shifts
  Logical shift
  Circular shift
  Arithmetic shift
What differentiates them is the information that goes into the serial input
A right shift operation
Serial input
A left shift operation
Serial input

## Slide 13: LOGICAL SHIFT
In a Register Transfer Language, the following notation is used
for a logical shift left
for a logical shift right
shl
shr
Examples:
R2  shr R2
R3  shl R3
In a logical shift the serial input to the shift is a 0.
A right logical shift operation:
0
A left logical shift operation:
0

## Slide 14: CIRCULAR SHIFT
In a circular shift the serial input is the bit that is shifted out of the other
end of the register.
A right circular shift operation:
A left circular shift operation:
In a RTL, the following notation is used
for a circular shift left for a circular shift right
cil
cir
Examples:
  R2  cir R2
  R3  cil R3

## Slide 15: Arithmetic Shift operation
An left arithmetic shift operation must be checked for the overflow
0
V
Before the shift, if the leftmost two bits differ, the shift will result in an overflow
In a RTL, the following notation is used
ashl
ashr
for an arithmetic shift left for an arithmetic shift right
– Examples:
» R2  ashr R2
» R3  ashl R3
sign bit

## Slide 16: Basic Symbols For Register Transfers
Symbols | Description | Examples
Capital letters | Denotes a register Denotes a part of a register Denotes transfer of information Denotes termination of control function Separates two micro-operations | MAR, R2
& numerals |  | 
Parentheses () |  | R2(0-7), R2(L)
Arrow  |  | R2  R1
Colon : |  | P: P2
Comma , |  | A  B, B A

## Slide 17: BUS AND Memory TRANSFER
Bus is a path(of a group of wires) over which information is transferred, from any of several sources to any of several destinations.
From a register to bus: BUS  R
1 | 2 | 3 | 4
1 | 2 | 3 | 4
1 | 2 | 3 | 4
Register A 1 2 3 4
Register B
Register C
Register D
B 1 C 1 D 1
B2 C 2 D 2
B 3 C 3 D 3
B4 C 4 D 4
4-line bus
x
y
select
0
4 x1 MUX
0
4 x1 MUX
0
4 x1 MUX
0
4 x1 MUX
Register A
Register B
Register C
Register D
Bus lines

## Slide 18: Transfer from Bus to destination register
Three-State Bus Buffers
Bus line with three-state buffers
Reg. R0
Reg. R1
Reg. R2
Reg. R3
Bus lines
Load
D 0 D1 D 2 D 3
2 x 4 Decoder
z
w
Select
E (enable)
Output Y=A if C=1
High-impedence if C=0
Normal input A Control input C
Select Enable
0
1
2
3
S0 S1
A0 B0 C0 D0
Bus line for bit 0

## Slide 19: Bus transfer in RTL
Depending on whether the bus is to be mentioned explicitly or not, register transfer can be indicated as either
R2  R1
or
BUS  R1, R2  BUS
In the former case the bus is implicit, but in the latter, it is explicitly indicated