## Slide 1: Pipelining conflicts & Pipeline Hazards

## Slide 2: Introduction:
Pipelining is a technique of breaking a sequential process into small fragments or sub-operations. The execution of each of these sub-procedure takes place in a certain dedicated segment that functions together with all other segments.
There are three types of Pipelining conflicts that are as follows −

## Slide 3: Resource Conflicts
These conflicts arise due to insufficient resources wherein it is not possible to overlap the operations.
Structural hazard occurs if two instructions need the help of a given hardware resource at an equal time. The most common situation in which this hazard occurs is when resources request for memory.

## Slide 4: Data Dependency Conflicts
These conflicts arise when the instruction in the pipeline depends on the result of the previous instructions and these instructions are still in pipeline and are not executed yet.
When either the source or the destination operand of an instruction is not available at the expected time in the pipeline, the pipeline is stalled. Such a situation is termed as a data hazard of data conflict.

## Slide 5: Data Dependency Conflicts: Example
Consider a program with two instructions, I1 followed by I2. When this program is executed in a pipeline, the execution of these two instructions is performed concurrently.
If the result of I1 and I2 are dependent on each other, then the result of I1 may not be available for the execution of I2.

## Slide 6: Branch Difficulties
This difficulty is faced when the branch and other instructions change the contents of the program counter.
There are two kinds of branches such as conditional and unconditional. Conditional branches may or may not cause branching but an unconditional branch always causes branching. This difficulty is termed a control hazard.

## Slide 7: Branch Difficulties
The following critical actions can be followed during the pipelining process which helps in handling control hazard −
Timely detection of a branch instruction
Early calculation of branch address
Early testing of branch condition (fate) for conditional branch instructions.

## Slide 8: Pipeline Hazards
Types of Pipeline Hazards in Computer Architecture
The three different types of hazards in computer architecture are:
1. Structural
2. Data
3. Control

## Slide 9: Structural Hazard
Hardware resource conflicts among the instructions in the pipeline cause structural hazards. Memory, a General purpose Register, or an ALU might all be used as resources here.
When more than one instruction in the pipe requires access to the very same resource in the same clock cycle, a resource conflict is said to arise.
In an overlapping pipelined execution, this is a circumstance where the hardware cannot handle all potential combinations.

## Slide 10: Data Hazards
Data hazards in pipelining emerge when the execution of one instruction is dependent on the results of another instruction that is still being processed in the pipeline.

## Slide 11: Control Hazards
Branch hazards are caused by branch instructions and are known as control hazards in computer architecture.
The flow of program/instruction execution is controlled by branch instructions. Remember that conditional statements are used in higher-level languages for iterative loops and condition testing (correlate with while, for, and if case statements).

## Slide 12: Control Hazards
These are converted into one of the BRANCH instruction variations. As a result, when the decision to execute one instruction is reliant on the result of another instruction, such as a conditional branch, which examines the condition’s consequent value, a conditional hazard develops.